## Slide 1: Smart Brite 36w 4000lumens Metal Batten
BN021 40s

## Slide 2: Positioning
High Brightness 36w 4000lm batten for commercial applications
Designed for parking spaces, go-downs and corridors/large spaces
Delivers 110 lumen/watt efficiency
Key Specs
36w 4000lm aluminium batten
Length – 4 feet
CRI > 80 for accurate colour rendering
Robust metal construction for better heat dissipation and longer life
Eye Comfort Technology with no blue light hazard
CCT: 6500k (CDL), 4000k (NW)

## Slide 3
Product Image
Diffuser:
Serrated Diffuser for wider light spread and better eye comfort
Construction:
Robust Aluminium channel for better heat dissipation & long life
User Safety:
Dedicated earthing provision and cable included in box for user safety

## Slide 4
Product Packaging
Product Tagline:
Superior LEDs. Lasting Performance
Product USP:
Best In Class LEDs. 110lm/watt efficiency
Focus on Application Areas:
Godowns. Parking Spaces

## Slide 5: Specifications
Lumen Output | 4000 Lm
System Wattage | 36 W
Efficacy | >110lm/watt
CCT | 6500K & 4000k
CRI | >80
Life Class | 20,000 hrs @ 35`C ambient temperature
Mounting | Wall/Surface
Housing | Aluminum Extrusion
IP | IP 20
Luminaire compliance | Relevant LED IS standards
Operating temperature | Up to 35 deg C
PF | > 0.9
THD | < 30 %
Input voltage range | 160V - 240V AC
diffuser | PC
Dimensions | 1185mm X 22mm X 36mm (approx.)
Serviceability | Non Replaceable Driver

## Slide 6: Ordering Code
12NC | Description
9195 158 13544 | BN 021 LED40S- 6500 PSU GR
9195 158 13723 | BN 021 LED40S- 4000 PSU GR
MRP | INR 1,499/-